## Slide 1
Machine Learning Models for Predictive Maintenance
A Comparative Study of Logistic Regression, Decision Trees, and Support Vector Machines (SVM) on the AI4I 2020 Dataset

## Slide 2
1. Logistic Regression: Working Principle
Linear Probability Modeling
Logistic Regression models the probability of binary machine failure using the Sigmoid activation function applied to a linear combination of sensor inputs.
Dataset Role: Evaluates individual continuous sensor features (Air/Process Temperature, Speed, Torque, Tool Wear).
Decision Boundary: Constructs a linear hyper-plane to divide normal operation from failure states.

## Slide 3
1. Logistic Regression: Pros & Cons
Advantages (Pros)
Disadvantages (Cons)
High Interpretability: Coefficients directly quantify the risk impact of each sensor metric (e.g., impact of +1 Nm torque).
Computational Efficiency: Extremely fast training and near-zero latency prediction for edge hardware.
Probabilistic Output: Returns continuous failure probabilities rather than strict binary decisions.
Linearity Assumption: Fails to capture non-linear failure triggers like Power Failure ( ).
Class Imbalance Sensitivity: Performs poorly on rare failure classes (3.39% in AI4I dataset) without reweighting.
Feature Interaction Limit: Cannot detect complex multi-sensor threshold combinations automatically.

## Slide 4
2. Decision Tree Classifier: Working Principle
Non-Linear Hierarchical Partitioning
Decision Trees recursively split the sensor feature space into axis-aligned rectangular decision regions using Information Gain or Gini Impurity reduction.
Capturing Complex Rules: Naturally replicates physical threshold conditions present in the AI4I dataset (e.g., If Tool Wear > 200 min AND Torque > 50 Nm → Overstrain Failure).
Non-Monotonic Split: Handles abrupt physical failure boundaries without needing mathematical transformation.
Feature Scale Invariant: Operates directly on unscaled raw sensor values (rpm, K, Nm, min).

## Slide 5
2. Decision Tree Classifier: Pros & Cons
Advantages (Pros)
Disadvantages (Cons)
Intuitive IF-THEN Logic: Visual decision rules map directly to maintenance engineer domain knowledge.
Automatic Feature Interactions: Detects multi-sensor conditions (e.g., Heat Dissipation Failure logic) naturally.
No Normalization Needed: Works seamlessly across different units without feature scaling.
High Variance & Overfitting: Unpruned trees easily memorize noise, causing poor generalization on new sensor telemetry.
Axis-Aligned Boundaries: Struggles with diagonal or smooth curved decision boundaries.
Instability: Small changes in operational sensor noise can drastically alter tree structure.

## Slide 6
3. Support Vector Machine (SVM): Working Principle
Maximum Margin Separation
SVM projects telemetry feature vectors into higher-dimensional space using Radial Basis Function (RBF) kernels to establish an optimal maximum-margin hyperplane.
Kernel Trick: Maps non-linearly separable failure clusters (e.g., Power Failures at high/low rpm bounds) into linearly separable space.
Cost Parameter ( ): Controls trade-off between maximizing margin width and penalizing misclassified failure instances.
Support Vectors: Focuses decision boundary solely on critical boundary samples near failure thresholds.

## Slide 7
3. Support Vector Machine (SVM): Pros & Cons
Advantages (Pros)
Disadvantages (Cons)
Superior Classification Accuracy: RBF Kernel achieves high F1-Scores on complex industrial multi-sensor data.
Robust in High Dimensions: Highly effective even with added engineered domain features.
Class Weight Customization: Cost penalization effective for handling AI4I's 3.39% failure class imbalance.
Black-Box Nature: Kernel transformations make decision boundaries difficult to interpret for shop-floor operators.
Computational Complexity: Training time scales quadratically with large streaming dataset size.
Strict Preprocessing Needed: Requires careful feature scaling (StandardScaler/MinMax) and hyperparameter tuning ( ).

## Slide 8
Thank You!
Questions & Discussion
Summary: Logistic Regression offers quick baseline interpretability, Decision Trees provide clear IF-THEN rules, and SVM delivers maximum predictive accuracy for non-linear failures.